Leica DISTO™ D2

Compact device – long range

| Small, handy, versatile! This small and handy laser distance meter has a range of 100 m and is equipped with many interesting functions. Measurements out of corners or from edges are no problem with the multi-functional end-piece. | Featured with: Bluetooth® Smart for data transfer to smart phones and tablets Multifunctional end-piece to measure out of corners and from edges 100 m range X­Range Power Technology Clear, illuminated 3 line display IP 54 dust and splash water protected |
| --- | --- |
| Bluetooth® Smart The latest Leica App DISTO™ sketch is the ideal link between the Leica DISTO™ D110 and a smartphone or tablet. With it you can prepare layouts and drawings, and dimension them precisely. | Multifunctional end-piece Whether measuring out of corners, slots or from edges, with this end-piece you are prepared for all measuring situations. The instrument detects the end-piece automatically, which helps to avoid expensive measuring errors. | Leica DISTO™ D2 Art. No. 837031 Leica DISTOTM D2 laser distance meter Holster Hand loop Batteries Technical Data Accuracy, typ. ± 1,5 mm Range 0.05 – 100 m Measuring units m, ft, in X-Rang Power Technology ( Display illumination ( Free App iOS, Android Data interface* Bluetooth® Smart Battery life time** up to 10‘000 measurements, up to 20h of operation Batteries type AAA, 2 x 1,5 V Protection class IP 54 Dimensions 116 x 44 x 26 mm Weight with batteries 100 g *) System requirements and details at www.disto.com **) Reduced in Bluetooth® Smart mode Functions Distance measurement Addition Subtraction Area measurement Memory (10 results) Automatic end-piece |
| Long distances With the help of the innovative X-Range Power technology this small device can measure long distances of up to 100 m. In addition, this technology ensures optimum measuring performance, i.e. fast and reliable measurements. | Useful functions Functions such as addition and subtraction, area and volume calculations make every measurement task child’s play. The instrument stores the last 10 measurement results. |  |